## Slide 1: Learning Energy Efficient Jumping Strategies for Flexible-Legged Systems
Andrew Albright, Joshua Vaughan
Dept. of Mechanical Engineering
Univ. of Louisiana at Lafayette
andrew.albright@louisiana.edu, joshua.vaughan@louisiana.edu

## Slide 2: Legged & Flexible Robots
Pros
  Ability to navigate uneven terrain
  Different designs can be useful for different tasks
  Can be designed to adapt to different terrain
Cons
  Difficult to design stable controllers
  Systems require high amounts of power
  Difficult to design to overcome different obstacles
https://www.bostondynamics.com/atlas
Notes: TODO:
Get citation

## Slide 3: Pros of Legged Robots
https://www.bostondynamics.com/atlas
Notes: TODO:
Get citation

## Slide 4: Legged & Flexible Robots
Pros
  Increases in efficiency
  Better stability through adaptability
  Higher performance
    Running speed
    Jumping height
Cons
  Difficult to define models for due to non-linearities
  Challenging to create controllers for
Notes: TODO:
Get citation

## Slide 5: Cons of Legged Robots
Watch the Atlas Robot take a spill running parkour #shorts - YouTube

## Slide 6: Control Methods
Traditional Controls Method
Reinforcement Learning Method
Notes: TODO:
Make sure your traditional controls diagram is correct

## Slide 7: RL Algorithm Used – TD3
Twin Delayed Deep Deterministic Policy Gradient
Can only be used with environments containing continuous action spaces
Off-policy learning algorithm
Actor-Critic Algorithm
Adds target policy smoothing
Learns main Q-function (critic) using two target Q-functions simultaneously
Updates the policy (actor), target policy and target Q-functions every two main Q-function updates

## Slide 8: Training Schedule
Task | Jump Type | # Agents | Network Seeds
Jump Hight | Stutter Jump | 10 | 9, 16, 104, 107, 250, 676, 868, 878, 918, 947
 | One Jump | 10 | 
Conserve Power | Stutter Jump | 10 | 
 | One Jump | 10 | 

## Slide 9: Flexible Jumping System
Model Parameter | Value
Mass of Leg, | 0.175 kg
Mass of Actuator, | 1.003 kg
Natural Frequency, | 11.13 Hz
Spring Constant, | 200000 N/m
Actuator Stroke, | 25 mm
Actuator Velocity, | 2.0 m/s
Actuator Acceleration, | 10 m/s
Model Parameter | Value
 | 0.175 kg
 | 1.003 kg
 | 11.13 Hz
 | 200000 N/m
 | 25 mm
 | 2.0 m/s
 | 10 m/s
Notes: TODO:
Consider making the plot in LaTeX

## Slide 10: Reward Functions
Learn to Jump High
Learn to Jump Efficiently

## Slide 11: Single Jump Expectation
Notes: Note:
Difference in timing for best agents
TODO:
What is a single jump?
Action? Observation?

## Slide 12: Single Jump Input
Notes: Note:
Difference in timing for best agents
TODO:
What is a single jump?
Action? Observation?

## Slide 13: Single Jump Height Reached
Notes: Note:
Best High agent jumped only 0.77% higher
0.61% higher average for high agent
0.76% higher max for high agent
17.91% more efficient average for the efficient agents
17.33% more efficient max for the efficient agent

## Slide 14: Single Jump Performance
Notes: Note:
Best High agent jumped only 0.77% higher
0.61% higher average for high agent
0.76% higher max for high agent
17.91% more efficient average for the efficient agents
17.33% more efficient max for the efficient agent

## Slide 15: Stutter Jump Expectations
Notes: Note:
- Difference in timing for best agents

## Slide 16: Stutter Jump Input
Notes: Note:
- Difference in timing for best agents

## Slide 17: Stutter Jump Height
Notes: Note:
Best Efficient agent jumped only 3.87% higher while also being 23.62% more efficient
2.22% higher average for eff agent
2.75% higher max for eff agent
10.56% more efficient average for the efficient agents
13.84% more efficient max for the efficient agent

## Slide 18: Stutter Jump Performance
Notes: Note:
Best Efficient agent jumped only 3.87% higher while also being 23.62% more efficient
2.22% higher average for eff agent
2.75% higher max for eff agent
10.56% more efficient average for the efficient agents
13.84% more efficient max for the efficient agent

## Slide 19: Conclusion
Reinforcement learning can be used to find control policies that are more efficient
Agents can learn efficient control where more complex control inputs are required
Controllers can be learned that are both higher in performance and efficient metrics

## Slide 20: Final Thoughts
Thank You!
Questions?